Course Name: Topics in ECE - Embedded Systems
Course Number and Section: 14:332:493:10

Experiment: [ Final Project ]
Lab Instructor: Professor Phillip Southard

Date Performed: -

Date Submitted: December 16, 2019

Submitted by: Antoni Chrobot	183008289

Final Project – Guitar Tuner
Github:

### Purpose
The purpose of my final project is to create a guitar tuner. My guitar tuner will play 7 different tones, based on user input, through the LINE OUT jack on the Zybo board. The 6 different tones will be played at frequencies which correspond to the standard tuning of a guitar (E A D G B e). A user will be able to select their desired frequency by setting the slide switches on the board to different values. The guitar tuner will also feature a seven segment display that will display the current string value that is selected.
### Theory of Operation
#### Tone generation
For the tone generation, I have decided to take a simple approach and re-use what I can from lab 3 (lab 5 in the Zynq book tutorials). In that lab we explored the use of custom made IP cores to interact with the audio codec. NCO (numerically controlled oscillator) was used to generate tones that were played through the LINE OUT jack on the board. I am using the NCO IP block to generate the tones, and will be modifying the software driver to meet my needs. The driver will be modified so that the values of the switches will map to a desired frequency for the generated tone.
#### Seven Segment Display
The seven segment display is a rather simple device. It contains seven LED segments. The seven segment display has 12 pins, two for power, two for ground, and the remaining eight pins are used for turning on or off each of the seven segments. To drive the seven segment display, I used a GPIO IP with 8 outputs. By writing the to the GPIO peripheral, I can easily display letters to the seven segment display.
### Principal IP Integrator Block Diagram

### Design

#include "adventures_with_ip.h"

int main(void)
{
        xil_printf("Entering Main\r\n");
        //Configure the IIC data structure
        IicConfig(XPAR_XIICPS_0_DEVICE_ID);

        //Configure the Audio Codec's PLL
        AudioPllConfig();

        xil_printf("SSM2603 configured\n\r");

        /* Initialise GPIO and NCO peripherals */
        gpio_init();
        nco_init(&Nco);

        xil_printf("GPIO and NCO peripheral configured\r\n");

        /* Display interactive menu interface via terminal */
        menu();
    return 1;
}
void menu(){
        u8 inp = 0x00;
        u32 CntrlRegister;

        /* Turn off all LEDs */
        Xil_Out32(LED_BASE, 0);

        XGpio_DiscreteWrite(&Gpio_audio_enable, 1, 0);

        CntrlRegister = XUartPs_ReadReg(UART_BASEADDR, XUARTPS_CR_OFFSET);

        XUartPs_WriteReg(UART_BASEADDR, XUARTPS_CR_OFFSET,
        ((CntrlRegister & ~XUARTPS_CR_EN_DIS_MASK) |
        XUARTPS_CR_TX_EN | XUARTPS_CR_RX_EN));

        xil_printf("\r\n\r\n");
        xil_printf("Embedded LMS Filtering Demo\r\n");
        xil_printf("Enter 's' to stream pure audio, 'n' to add tonal noise and 'f' to adaptively filter\r\n");
        xil_printf("----------------------------------------\r\n");

        // Wait for input from UART via the terminal
        while (!XUartPs_IsReceiveData(UART_BASEADDR));
        inp = XUartPs_ReadReg(UART_BASEADDR, XUARTPS_FIFO_OFFSET);
        // Select function based on UART input
        switch(inp){
        case 's':
        xil_printf("STREAMING AUDIO\r\n");
        xil_printf("Press 'q' to return to the main menu\r\n");
        XGpio_DiscreteWrite(&Gpio_audio_enable, 1, 1);
        audio_stream();
        break;
        case 'n':
        xil_printf("ENTERING NOISE GENERATION OPERATION\r\n");
        xil_printf("Select step size via the DIP switches...\r\n\n");
        xil_printf("Press 'q' to return to the main menu\r\n");
        XGpio_DiscreteWrite(&Gpio_audio_enable, 1, 1);
        tonal_noise();
        break;
        case 'f':
        xil_printf("ENTERING LMS FILTERING OPERATION\r\n");
        xil_printf("Press 'q' to return to the main menu\r\n");
        XGpio_DiscreteWrite(&Gpio_audio_enable, 1, 1);
        lms_filter();
        break;
        default:
        menu();
        break;
        } // switch
} // menu()

### Test

### Implementation

Elaboration schematic
### Synthesis schematic
### On-chip power graphs
### Utilization table
### Discussion